## Slide 1: Water right modeling in SWAT+

## Slide 2
Parameters
: Parameters from the OWRD WR data source
: Parameters calculated using parameter in the OWRD WR data source
: Other data sources
: User-defined Parameters
: Optional Parameters
POD ID: Unique ID set by user for each unique POD in the WR database.
Water Use Code: 23 POU categories.
Source Type: Where the water comes from (Opt. 1. Channel, 2. Reservoir, 3. Aquifer shallow, 4. Deep Aquifer, 5. External to watershed)
Source ID: ID number of Source obj (ex. Cha1)
Minimum Source Volume (acre-feet): Dead level of reservoir converted to volume.
Priority Date: Set the water allocation priority based on this date.
Start/End Date: Water right application span, used for calculation of Allowed Maximum Volume.
Maximum Volume Allowed: Acre-feet unit Withdrawal rate, pre-calculated by user using OWRD WR data (Start/End Date, available Withdrawal rate or volume stated in water right)
Compensation options: If this Point of Diversion (POD) has an alternative water source to use when it suffers shortage, we can refer to the other source as a compensatory source. (Opt. Absence, Exist)
Return Delay: How long it takes for water (return flow) to go back to a stream or an aquifer.
Return Source: The location where water used by a consumer is transported or returned.
Return Rate (%): The rate of water returned to the system after use. (Any water not returned to the system at this rate is considered consumptive use and is completely removed from the watershed.)
Domestic Duty: Duty for Domestic use. Acre-feet per family unit.
Family Number: The number of family which utilized the water right. You can get this at the WR certification or Permit. (If available.)
Irrigation Duty: Duty for Irrigation use. Acre-feet/feet unit.
Irrigation Area: You can get this at the WR certification or Permit.
Livestock Duty: Duty for Livestock use. Acre-feet/feet unit.
ELU:
Water use code
1. Aesthetics
2. Agriculture uses
3. Anadromous and resident fish habitat (instream)
4. Commercial uses
5. Domestic
6. Domestic and livestock
7. Domestic expanded
8. Domestic including lawn and garden
9. Fire protection
10. Fish culture
11. Forest management
12. Human consumption
13. Industrial/manufacturing uses
14. Irrigation
15. Irrigation and domestic
16. Livestock
17. Mining
18. Multiple instream uses
19. Municipal uses
20. Pond maintenance
21. Power development
22. Storage
23. Wildlife
ELU
1. Cow or horse: 0.028 acre-foot
2. Sheep, goat, swine, moose, or elk: 0.0056 acre-foot
3. Ostrich or emu: 0.0036 acre-foot
4. Llama: 0.0022 acre-foot
5. Deer, antelope, bighorn sheep, or mt. Goat: 0.0014 acre-foot
6. Chicken, turkey, chukar, Sagehen, or pheasant: 0.00084 acre-foot
7. Mink or fox (caged): 0.00005 acre-foot
Model Set-up – Description of Parameters

## Slide 3
Implement 1 – Domestic from Channel
Func. Water_Allocation (POD_ID, Water_Use_Code, Source_type, Source_ID, ..., Maximum Volume Allowed)
For day in operation period
Updated_ Maximum_Volume_Allowed = Cut_off ()
For current POD_ID in POD_list
Maximum_Volume_Allowed(current POD_ID, day) = Updated_ Maximum_Volume_Allowed (current POD_ID)
If Water_Use_Code == 5 ~ 8 { # Water Use Code for Domestic.
If Source_Type == 1 { # Source_ID is linked with the pre-defined Channel_ID or Reach_ID.
If day >= start_date and <= end_date {
If SWAT_flowout (day, source_id) >= Maximum_Volume_Allowed / (end_date - start_date) {
Withdrawal = Maximum_Volume_Allowed / (end_date - start_date) # Daily volume allowed for domestic use.
Deficit = 0;
Else
Withdrawal = SWAT_flowout (Day, source_id) }}}}} # Assigning Total flow for domestic.
Deficit = Maximum_Volume_Allowed / (end_date - start_date) - Withdrawal
SWAT_flowout (Day, source_id) = SWAT_flowout (Day, source_id) – Withdrawal # Updating the channel flow.
POD ID | Water Use Code | Source Type | Source ID | Minimum Source Volume | Priority Date | Start Date | End Date | Maximum Volume Allowed
1 | 5 | 1 | Cha1 |  |  |  |  | 
Domestic Duty | Family Number |  |  |  |  | Return Delay | Return Source | Return Rate

## Slide 4
Implement 1 – Domestic from Channel
Def Cut_off (POD_list, start_date, end_date) {
For POD_list {
If Water_Use_Code == 5 to 8 { # Water Use Code for Domestic.
If Domestic_Duty > Maximum_Volume_Allowed { # If they have a duty, use duty as Maximum Volume Allowed.
Maximum_Volume_Allowed = Domestic_Duty * Family_Number }}
If Water_Use_Code == 14 or 15 { # Water Use Code for Irrigation.
If Irragation_Duty > Maximum_Volume_Allowed { # If they have a duty, use duty as Maximum Volume Allowed.
Maximum_Volume_Allowed = Irrigation_Duty * Irrigation_Area }}
If Water_Use_Code == 16 { # Water Use Code for livestock.
If Livestock_Duty > Maximum_Volume_Allowed { # If they have a duty, use duty as Maximum Volume Allowed.
  If Stock_Type == 1 (Cow or Horse) {
  ELU = 0.028 # Equivalent Livestock Unit.
  Else
  Maximum_Volume_Allowed = Livestock_Duty * ELU * Number_Livestock }}}
Cutoff_List = Sort(POD_List, priority)
For POD_i in Cutoff_List {
If Cutoff_List(POD_i, Deficit)> 0 { # Deficit > 0.
Continue }
For POD_J in Cutoff_List(POD_i : end, 1)
if (check_if_upstream(POD_J, POD_i) & check_if_protected(POD_J not in protected_types)
candidates.append((POD_J, POD_i)
For j_idx in candidates (:, POD_i) {
If Cutoff_List(POD_i, Deficit) <= 0 {
Break }
If Cutoff_List(j_idx, Maximum_Volume_Allowed) <= Cutoff_List(i, deficit)
Cutoff_List(i, deficit) = Cutoff_List(i, deficit) - Cutoff_List(j_idx, Maximum_Volume_Allowed)
Cutoff_List(j_idx, Maximum_Volume_Allowed) = 0 # Set junior withdrawal to 0.
Else:
Cutoff_List(j_idx, Maximum_Volume_Allowed) = Cutoff_List(j_idx, Maximum_Volume_Allowed) - Cutoff_List(i, deficit) # Decrease junior withdrawal.
Cutoff_List(i, deficit) = 0
Return Cutoff_List

## Slide 5
Implement 1 – Domestic from Channel
Optional “Return Flow” Function
If Water_Use_code == 1, 3, 10, 18, 21 { # Water remains within the channel or wetland complex, maintaining the mass balance of the reach.
Receiving_Source = 0 }
If Water_Use_code == 2, 8, 11, 14, 15, 23 { # Used for agriculture or nature; a portion infiltrates into groundwater and consume via crop evapotranspiration (ET).
Receiving_Source = 1 }
If Water_Use_code == 5, 6, 7, 12, 19 { # Used for human consumption; no return flow.
Receiving_Source = 0 }
If Water_Use_code == 4, 13, 16, 17 { # Used for Industrial and Energy Development; no return flow.
Receiving_Source = 0 }
If Water_Use_code == 9, 20, 22 { # Used for storage maintenance; no return flow. Receiving_Source = 0
If Receiving_Source == 0
Return_Flow = 0 # Water is permanently removed from the watershed balance.
Elseif Receiving_Source == 1
Return_Flow = Withdrawal * Return_Rate # A portion of water is re-introduced.
SWAT_flowout (jday+time_delay, source_id) = SWAT_flowout (jday+time_delay, source_id) + Return_Flow # Water is re-introduced to the original source after a time delay.
Else (Receiving Type == 2)
Return Flow = Withdrawal # Entire Water is re-introduced.
SWAT_flowout (day+time_delay, return_source_id) = SWAT_flowout (day+time_delay, return_source_id) + Return_Flow } # Water is re-introduced to a specific designated source.

## Slide 6
Implement 2 – Instream from Channel
Func. Water_Allocation (POD_ID, Water_Use_Code, Source_type, Source_ID, ..., Maximum Volume Allowed)
For Day in operation period
Updated_ Maximum_Volume_Allowed = Cut_off ()
For current POD_ID
Maximum_Volume_Allowed(current POD_ID, Day) = Updated_ Maximum_Volume_Allowed (current POD_ID)
If Water_Use_Code == 3 or 18 { # Water Use Code for Instream.
If Source_Type != 1 { # Source_type for instream should be the Channel.
Break
Else
If Day >=start_date and <= end_date {
If SWAT_flowout (Day, source_id) >= Maximum_Volume_Allowed / (end_date - start_date) {
Instream_Flow (Day, source_id) = Maximum_Volume_Allowed / (end_date - start_date) # Daily volume allowed for domestic use.
Else
Instream_Flow (Day, source_id) = SWAT_flowout (Day, source_id) }}}}} #Total flow
Deficit = Maximum_Volume_Allowed / (end_date - start_date) - Instream_Flow (Day, source_id)
POD ID | Water Use Code | Source Type | Source ID | Minimum Source Volume | Priority Date | Start Date | End Date | Maximum Volume Allowed
2 | 3 or 18 | 1 | Cha1 |  |  |  |  | 
 |  |  |  |  |  | Return Delay | Return Source | Return Rate

## Slide 7
Implement 3 – Domestic from Reservoir
Func. Water_Allocation (POD_ID, Water_Use_Code, Source_type, Source_ID, ..., Maximum Volume Allowed)
For Day in operation period
Updated_ Maximum_Volume_Allowed = Cut_off ()
For current POD_ID
Maximum_Volume_Allowed(current POD_ID, Day) = Updated_ Maximum_Volume_Allowed (current POD_ID)
If Water_Use_Code == 5 { # Water Use Code for Domestic.
If Source_Type == 2 { # Source_ID is linked with the pre-defined Channel_ID or Reach_ID.
If Day >=start_date and <= end_date {
If Storage_Volume (Day, source_id) - Minimum Source Volume (source_id) >= Maximum_Volume_Allowed / (end_date - start_date) {
Withdrawal = Maximum_Volume_Allowed / (end_date - start_date) # Daily volume allowed for domestic use.
Deficit = 0;
Else
Withdrawal = Storage_Volume (Day, source_id) - Minimum Source Volume (source_id) }}}}} #Total flow
Deficit = Maximum_Volume_Allowed / (end_date - start_date) - Withdrawal
Storage_Volume (Day, source_id) = Storage_Volume (Day, source_id) – Withdrawal # Updating the channel flow
POD ID | Water Use Code | Source Type | Source ID | Minimum Source Volume | Priority Date | Start Date | End Date | Maximum Volume Allowed
3 | 5 | 2 | Res1 | Dead level |  |  |  | 
Domestic Duty | Family Number |  |  |  |  | Return Delay | Return Source | Return Rate

## Slide 8
For Day in operation period
Updated_ Maximum_Volume_Allowed = Cut_off ()
For current POD_ID
Maximum_Volume_Allowed(current POD_ID, Day) = Updated_ Maximum_Volume_Allowed (current POD_ID)
If Water_Use_Code == 14 or 15 { # Water Use Code for Irrigation.
If Source_Type == 1 { # Source_ID is linked with the pre-defined Channel_ID or Reach_ID.
If Day >=start_date and <= end_date {
If SWAT_flowout (Day, source_id) >= Maximum_Volume_Allowed / (end_date - start_date) {
Withdrawal = Maximum_Volume_Allowed / (end_date - start_date) # Daily volume allowed for domestic use.
Deficit = 0;
Else
Withdrawal = SWAT_flowout (Day, source_id) }}}}} #Total flow
Deficit = Maximum_Volume_Allowed / (end_date - start_date) - Withdrawal
SWAT_flowout (Day, source_id) = SWAT_flowout (Day, source_id) – Withdrawal # Updating the channel flow
Implement 4 – Irrigation from Channel
Func. Water_Allocation (POD_ID, Water_Use_Code, Source_type, Source_ID, ..., Maximum Volume Allowed)
POD ID | Water Use Code | Source Type | Source ID | Minimum Source Volume | Priority Date | Start Date | End Date | Maximum Volume Allowed
4 | 14, 15 | 1 | Cha1 |  |  |  |  | 
Irrigation Duty | Irrigation Area |  |  |  |  | Return Delay | Return Source | Return Rate

## Slide 9
For Day in operation period
Updated_ Maximum_Volume_Allowed = Cut_off ()
For current POD_ID
Maximum_Volume_Allowed(current POD_ID, Day) = Updated_ Maximum_Volume_Allowed (current POD_ID)
If Water_Use_Code == 16 { # Water Use Code for Domestic.
If Source_Type == 1 { # Source_ID is linked with the pre-defined Channel_ID or Reach_ID.
If Day >=start_date and <= end_date {
If SWAT_flowout (Day, source_id) >= Maximum_Volume_Allowed / (end_date - start_date) {
Withdrawal = Maximum_Volume_Allowed / (end_date - start_date) # Daily volume allowed for domestic use.
Deficit = 0;
Else
Withdrawal = SWAT_flowout (Day, source_id) }}}}} #Total flow
Deficit = Maximum_Volume_Allowed / (end_date - start_date) - Withdrawal
SWAT_flowout (Day, source_id) = SWAT_flowout (Day, source_id) – Withdrawal # Updating the channel flow
Implement 5 – Livestock from Channel
Func. Water_Allocation (POD_ID, Water_Use_Code, Source_type, Source_ID, ..., Maximum Volume Allowed)
POD ID | Water Use Code | Source Type | Source ID | Minimum Source Volume | Priority Date | Start Date | End Date | Maximum Volume Allowed
5 | 16 | 1 | Cha1 |  |  |  |  | 
Livestock Duty | Livestock Type | Livestock number |  |  |  | Return Delay | Return Source | Return Rate